ANNEX A

CHANGES TO 446 MHZ AND 5 GHZ FREQUENCY BANDS

Table 1: Summary of Changes for 5 GHz Frequency Bands

|  | Wireless Local Area Network (WLAN) Frequency Allocations | Power Limit |
| --- | --- | --- |
| Previously | Bands allocated for WLAN deployment: 5150 – 5250 MHz 5725 – 5850 MHz | 5150 – 5250 MHz = 100 mW (e.i.r.p.) 5725 – 5850 MHz = 100 mW (e.i.r.p.) |
| Now | Additional bandwidth for WLAN deployment: 5250 – 5350 MHz | 5150 – 5350 MHz = 200 mW (e.i.r.p.) 5725 – 5850 MHz = 100 mW (e.i.r.p.) |

Figure 1: Changes to Spectrum Allocation

400 to 824 MHz

| Meteorological Services | Mobile Data, PMR & Trunking | TV Band IV CH24 – CH 38 | TV Band V CH39 – CH 60 | Fixed | Mobile Data, PMR & Trunking | LP Devices |
| --- | --- | --- | --- | --- | --- | --- |

400	       406			           490					 614				        790	        806		    821	               824

446.0	      446.1

1880 to 10680 MHz

| DECT & PHS | IMT-2000 | MSS | IMT-2000 | MSS | Fixed | LP Devices | Fixed | Mobile | Radio-navigation | Fixed Satellite | Fixed | Radio-navigation | Fixed Satellite | Fixed | Radio-navigation | Fixed & Satellite |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
|  |  |  | Fixed |  | Mobile |  |  |  |  |  |  |  |  |  |  |  |

1880       	1900   1980                 2010         	        2170         2220                  2400     2483.5   2690 		3400       4200      5000              5850             7075   8500              10680                         71000

5150               5250               5350             5725              5850

# Text boxes

Low-powered Walkie-talkies

NEW!!

NEW!!

WLAN

WLAN

WLAN